## Slide 1: Geomorphometry I: Terrain modeling
Geospatial Analysis and Modeling:
Lecture notes
Helena Mitasova, NCSU MEAS

## Slide 2: Outline
Definitions
3D mapping technologies
mathematical and digital terrain models
point clouds, multiple return data
triangular irregular networks
regular grid (raster)
isolines and meshes
point cloud analysis and binning

## Slide 3: Definitions
Land (bare earth) surface: interface between solid Earth and atmosphere/anthroposphere/biosphere
Terrain surface : interface between Earth with water, vegetation, structures and atmosphere
Bathymetry: interface between solid Earth surface and hydrosphere (bottom surface of lakes, rivers and ocean)
Seamless topobathy: continuous solid earth surface
Notes: Intro - this has been already covered

## Slide 4: Bare Earth and Terrain surface
Terrain surface:
bare ground + vegetation and structures
Bare ground surface
Notes: Intro - this has been already covered

## Slide 5: Bathymetry
Nearshore bathymetry
Bathymetry:
sand disposal
Notes: Intro - this has been already covered

## Slide 6: Seamless topobathy
Notes: Intro - this has been already covered

## Slide 7: Mathematical terrain models
Mathematical representations of bare Earth surface:
bivariate function (for each x,y there is only one value of z):
z = f(x,y)
Notes: Intro - this has been already covered

## Slide 8: Mathematical terrain models
Mathematical representations of bare surface:
bivariate function:
z=f(x,y)
non-stationary signal consisting of multiscale components
z(x,y)=S(x,y)+Dj(x,y)+Dj-1(x,y).....D1(x,y)
where S(x,y) is the smoothest component, Di (x,y) are progressively more detailed components
deterministic component zd +random spatially correlated error + noise
z(x,y)=zd(x,y)+e'(x,y)+e”(x,y)
Notes: Intro - this has been already covered

## Slide 9: Multiscale terrain components
Terrain profiles at different level of detail
Sand dune vegetated area
z(x,y)=S(x,y)
z(x,y)=S(x,y)+Dj(x,y)
Notes: Intro - this has been already covered

## Slide 10: Mathematical terrain models
Is the bivariate function representation general enough?
General 3D surface defined using
parametric representation: x=f(u,v), y=g(u,v), z=h(u,v,),
Supported by K3DSurf, CAD
GIS: 3D vector model
Notes: Intro - this has been already covered

## Slide 11: Terrain mapping technologies
Continuous surface measured at discrete points
Human selected points (GPS, total station, photogrammetry)
Automated point sampling (lidar, RTK GPS, sonar)
Land terrain mapping
Stereophotogrammetry: mass points and breaklines
IFSARE: raster, Lidar: point cloud
On-ground 3d laser scanner: point cloud
RTK GPS: point profiles
Bathymetry mapping
single and multiple beam sonar
Notes: Intro - this has been already covered

## Slide 12: Mapping Technology: land
RTKGPS
On-ground laser scanner
LIDAR: Light Detection
and Ranging
USGS/NOAA/NASA
ATM-II, EAARL
Haiti LIDAR:http://www.wired.com/wiredscience/2010/01/haiti-3d-flyover/

## Slide 13: Mapping technology: bathymetry
Bathymetry:
multibeam sonar
Nearshore Bathymetry:
single beam sonar
Notes: Add here slide with unmanned lidar

## Slide 14
Elevation data: point distribution

## Slide 15: Elevation data: accuracy

## Slide 16
substantially improved
representation of structures
but much larger data sets
1m res. DEM, computed by RST, 1998 lidar data
2004 lidar, 0.5m resolution DEM
binned and computed by RST
(smoothes out the noise and fills
in the gaps)

## Slide 17: Coastal airborne lidar: 1996 - 2011
1998
2004
Agency Year pts/1m cell
NOAA/NASA/USGS 1996 0.1
NOAA/NASA/USGS 1997 0.3
NOAA/NASA/USGS 1998 0.2
NOAA/NASA/USGS 1999 0.4
NC Floodplain 2001 0.1
NASA/USGS 2003 0.6
USACE Topobathy 2004 4.0
USACE Topobathy 2005 1.2
NSF NCALM UoF 2006 1.0
NSF NCALM UoF 2007 1.0
NOAA 2008 1.0
USGS 2009 5.0
USACE 2010
NOAA 2011
1m res. DEM, computed by RST, 1998 lidar data
2004 lidar, 0.3m DEM
computed by RST
100m
point density and spatial coverage
varies for each survey

## Slide 18: Ground based laser scanner data
0.1m res. DEM and rgb image
Point cloud and image

## Slide 19
Hatteras Island before
And after Isabel 2003
Bathy-topo survey
of the breach:
single beam sonar
RTK GPS
semiautomated
point selection
Elevation data: beach and bathymetry

## Slide 20
Post Isabel Hatteras Breach

## Slide 21: Digital terrain representations
Point clouds – measured data
TIN – Triangular Irregular Network
Regular grid (raster)
Contours - elevation isolines
Mesh
Notes: Intro - this has been already covered

## Slide 22: Point clouds
Set of (x, y, z, r, i, ...) measured points reflected from Earth surface or objects on or above it, where x,y,z are georeferenced coordinates, r is the return number and i is intensity, r:g:b may be also measured
Provided in
  ASCII (x,y,z, ...) format
  binary LAS format (header, record info, x,y,z,i, scan dir, edge of flight line, classification, etc.), industry lidar data exchange format
Notes: Intro - this has been already covered

## Slide 23: Point clouds
Processing:
  filtering outliers (birds etc.)
  bare earth point extraction
  canopy extraction
  structures and power lines extraction
Public data sources (http in Summary slide):
CLICK: raw point clouds usually in LAS format
LDART: costal point clouds with on-fly binning
NC Floodplain Mapping: bare Earth: points, 20ft DEM and 50ft DEM with carved channels
Notes: Intro - this has been already covered

## Slide 24: Point clouds
Multiple return point cloud data from 2001 NC Flood mapping program – yellow is first return
Image from LIDAR primer, Geospatial solutions 2002
Notes: Intro - this has been already covered

## Slide 25: TIN
Triangular Irregular Network: constructed from the measured points by triangulation (before computer age this technique was used for manual interpolation of contours from surveyed points)
Delaunay Triangulation: maximizes the smallest angle of the triangles to avoid skinny triangles
Constrained Delaunay Triangulation – includes predefined edges that cannot be flipped
TIN is a vector data model representation, that usually preserves the original data points
Notes: Intro - this has been already covered

## Slide 26: TIN
Given points Delaunay TIN
Notes: Intro - this has been already covered

## Slide 27: TIN
Delaunay TIN from random points and contour points
Notes: Intro - this has been already covered

## Slide 28: TIN properties
requires pre-defined breaklines for man-made features, valleys, faults, etc.
density of TIN is adjusted to surface complexity
additional points may need to be interpolated to create smooth surface
When to use TIN:
engineering applications,
manual modification of model is desired(design),
complex faults need to be represented,
multiscale representation for visualization
Notes: Intro - this has been already covered

## Slide 29: TIN issues
discontinuity in first derivative along edges: artificial triangular structures on the surface
dams can be created across valleys if stream is not defined as a breakline
if input are points on contours: flats on the top of hills or ridges if no peaks are defined
Image by
TERRASTREAM
Dept. of Computer Science,
Duke University
Notes: Intro - this has been already covered

## Slide 30: Regular grid - raster
Two interpretations:
elevation assigned to a grid point – center of the grid cell
elevation assigned to the pixel area
Derived from measured points by gridding:
at least one point for each grid cell – binning,
if some grid cells do not include points – spatial interpolation or approximation
Notes: Intro - this has been already covered

## Slide 31: Regular grid - raster
Given Points Regular Grid
Notes: Intro - this has been already covered

## Slide 32: Regular grid: properties
simple data structure and algorithms
easy to combine with imagery
uniform resolution - potential for undersampling and oversampling
representation of faults and sharp breaklines requires very high resolution
Notes: Intro - this has been already covered

## Slide 33: Regular grid -public data
Most available elevation data are distributed as raster data:
USGS Seamless Data Distribution
  NED 1/9 (3m),1/3 (10m),1 arc/sec (30m),
SRTM-V4: USA 30m, World 90m
GDEM 15-30m: global, relative height, derived from ASTER satellite stereo bands
NCFlood mapping web site: 20ft and 50ft DEM
CRM for bathymetry: 90m
Seamless Topobathy: Tsunami data and RENCI NC data - 10m
Notes: Intro - this has been already covered

## Slide 34: Isolines, contours
traditional approach for representation of elevation, drawn by hand from measured mass points by interpolating along triangle edges
automated procedures: from TIN or grid,
not very suitable for highly detailed, noisy data such as lidar
needed when the surface has simple geometry
selecting contour interval: depends on slope and resolution
Notes: Intro - this has been already covered

## Slide 35: Isolines, contours
Contours from lidar

## Slide 36: Point cloud analysis: binning
Binning: fast method for analyzing point clouds and generating DEMs using per-cell processing:
at least one point for each grid cell
analysis: number of points per cell, range, stddv
Methods for DEM: mean, min, max, nearest
sufficient for many applications
no need to import the points, on-fly raster generation
may be noisy, include no-data spots
Notes: Intro - this has been already covered

## Slide 37: Point cloud analysis: input
Multiple return point cloud
all returns
first return
Notes: Intro - this has been already covered

## Slide 38: Point cloud analysis: input
Bare earth and multiple return point cloud
all returns
bare earth
Notes: Intro - this has been already covered

## Slide 39: Point density
Number of bare earth points in each 2m and 6m resolution cell
Number of points
from ground based scan
in each 40cm grid cell
Notes: Intro - this has been already covered

## Slide 40: Points per-cell elevation range
Range of bare earth elevations zmax-zmin in each cell at 6m resolution
Notes: Intro - this has been already covered

## Slide 41: Points to grid: per-cell mean
Mean bare earth elevation for each 6m cell
Not enough bare earth
points : interpolation
is needed
Interpolated DEM and DSM
at 1m resolution
Notes: Intro - this has been already covered

## Slide 42: Lidar data examples: 2013 Raleigh
0793_016.las tile point densities
Number of all return and bare earth points in each 1m (3ft) cell
Notes: Intro - this has been already covered

## Slide 43: Lidar data examples: 2013 Raleigh
interpolated bare earth
and first return surfaces
Notes: Intro - this has been already covered

## Slide 44: Lidar data examples: 2013 Raleigh
interpolated first return surface with orthophoto draped
over it: note the outlier and power lines
Notes: Intro - this has been already covered

## Slide 45: Lidar data example: coastal
Number of points in each 2m resolution cell for 2001 and 2004 lidar survey near Oregon Inlet
1
7
14
21
28
35
Notes: Intro - this has been already covered

## Slide 46: Points per-cell elevation range
Range of elevations zmax-zmin in each cell at 0.3, 1., 5. and 10m resolutions – 2004 lidar near Oregon Inlet
5m
4
3
2
1
0
Notes: Intro - this has been already covered

## Slide 47: Road lidar data: 2012
New mobile terrestrial lidar road survey for all NC coastal counties
scan lines: 15-20cm
masked 10cm resolution DEMs
captures road profile
2001 1m res. DEM, 2012 0.1m res. road DEM
airborne + terrestrial
I-158 NC-12
20m
10m
Thanks to Doug Newcomb and Hope Morgan for sharing the data
Notes: Road lidar 15cm profiles, sub 1cm along profile

## Slide 48: Lidar data examples: JR binning
Jockey's Ridge 1999, unfiltered single return lidar point cloud: 1m grid cell binning using maximum elevation
Result has many NULL cells – what to do?
Notes: Intro - this has been already covered

## Slide 49: JR 1999 lidar: binning
3m grid cell binning: points to grid with method mean
Notes: Intro - this has been already covered

## Slide 50: JR lidar: interpolated DSM
1m DEM interpolated by splines – see next lectures
Notes: Intro - this has been already covered

## Slide 51
Dr. Mike Starek, Nathan Lyons, Keren Cepero, Dr. Wegmann
Talk EP33D-06: Wednesday
Legacy sediment from old millpond
monitoring by Leica Scan TCL:
9 epochs 2010 – 2012
1cm resolution bank surface
represented as tilted DEM
Monitoring eroding stream bank
distance to base plane [m]
first and last survey

## Slide 52: Summary and references
Mathematical and digital terrain representation
  Neteler Ch. 5,6; Hengl Ch. 2,
Point clouds and TIN
  Neteler Ch.6.; Hengl et al. Geomorphometry
Regular grids
  Neteler Ch. 7, Hengl
Isolines and meshes
  Neteler Ch. 5, Hengl
LIDAR: http://www.forestry.gov.uk/forestry/INFD-6RVC9J
http://www.geospatial-solutions.com/geospatialsolutions/article/articleDetail.jsp?id=10275
Learn more about Lidar in MEA592-004/GIS595-002:
Multidimensional Geospatial Modeling