## Slide 1: Airborne Topographic LiDAR Systems:
Michael Starek

## Slide 2: Outline
Introduction
System Components / Types
Data Products
Data Artifacts and Error Sources
System Examples

## Slide 3: Introduction

## Slide 4: History of LiDAR Mapping
Light Detection and Ranging (LiDAR)
  Geodimeter: 1953
  Gould coins the term LASER: 1959
  Lunar laser ranging: 1960’s
  Early NASA airborne lidar prototypes: 1970’s
  Integrated GPS/IMU navigation: late 1980’s to 90’s
    gave rise to modern airborne LiDAR systems
Other names for Airborne LiDAR
  Airborne Laser Scanning (ALS)
  Airborne Laser Swath Mapping (ALSM)
  Laser Altimetry - NASA
  Laser Radar (LADAR) – military

## Slide 5: Basic Principle
Pulse Ranging
Fire a laser pulse from transmitter mounted in aircraft and capture reflected energy
Measure round trip time-of-travel (Tl ) to determine range to target
  Speed of light c ~= 3 x 108 m/s  Range = Tl / 2 * c
Laser
Receiver
Reflector
outgoing pulse
return pulse

## Slide 6
Post-Processing
Image from International Summer School “Digital Recording and 3D Modeling”, Claus Brenner 2006.
Lidar Equation
Relates transmit to received power
Example

## Slide 7: LiDAR Final Outputs
Geolocated point cloud
  Irregularly distributed x,y,z values in 3D space representing the location of reflection objects
Intensity
  Relative measure of reflection energy (watts/m2)
  *Note: Varies by system, some do not record (e.g. photon-counting LiDAR)
Point Cloud
Intensity Plot
Elevation =color
Brightness = intensity

## Slide 8: Overview of Airborne Lidar Systems

## Slide 9: 3 Main Components
Laser ranging unit laser transmitter, scanner, receiver
Position Orientation System (POS) GPS & Inertial Measurement Unit (IMU)
Control and Data Acquisition Unit
Image from Claus Brenner 2006.
Scanner Swath

## Slide 10: Scanning Mechanisms
Image from International Summer School “Digital Recording and 3D Modeling”, Claus Brenner 2006.
e.g. TopEye MK II
e.g. NASA EAARL , Optech ALTM (most common)
e.g. TopoSys Falcon III
e.g. IGI LM 6800

## Slide 11: Prism Scanning
Risley Prism Scanner
(index of refraction)
Example of Scan Patterns
Can generate various scan patterns dependent on rotational prism offset.
e.g. CATS UF bathymetric system

## Slide 12: LiDAR System Classification
Topographic
Bathymetric
Discrete Return
Full Waveform
Photon Counting
Small footprint
Large footprint

## Slide 13: Topographic vs Bathymetric
Topographic Systems
  Typically operate in Near-IR range of EM spectrum
    Reflective over common terrain surfaces (e.g. green vegetation)
    E.g. 1064 nm λ, Nd:YAG solid-state laser
Bathymetric Systems
  Blue-green penetrates water. Near-IR is mostly absorbed.
    E.g. 532 nm λ, frequency doubled Nd:YAG laser
  Penetration upwards of 40+ m
    Depends heavily on water clarity and bottom reflectivity
Principle of bathymetric lidar showing refraction of light in water
Image from Dr, Bharat Lohani; http://home.iitk.ac.in/~blohani/LiDAR_Tutorial

## Slide 14: Spectral Reflectance of Various Target Types
Image from Optech 2007
High grass reflectivity in near-IR
Higher reflectivity in water for blue-green wavelength

## Slide 15
Attenuation Coefficient of Water
Image adapted from Tyler and Preisendorfer ,1962
Less attenuation of blue-green light

## Slide 16: Ranging Methods
Discrete return
  Logs time when return intensity exceeds threshold
  Common for commercial systems
  Pros: Quick hardware
  Cons: no flexibility; elevation bias on short vegetation
  Waveform recording
  digitize entire return intensity profile (waveform)
  Pros: processing flexibility; canopy mapping
  Cons: info-overload potential
  Photon counting
  Records individual photons
  Pros: low power, good cloud penetration, map higher
  Cons: sensitive to ambient noise
Image from Dave Harding, NASA

## Slide 17: Discrete Return Detection
Constant Fraction Discriminator (CFD)
  Leading edge set as a constant fraction of return peak amplitude
    Hardware implemented
    Measured time not impacted by signal peak
    Rise time and signal convolution can cause range errors
    E.g. range walk
Example showing CFD travel time impacted by pulse rise times -> can cause range walk
T = time
Return signals

## Slide 18
Example of discrete system with maximum of 4 returns per pulse
Image modified from USGS; Hans-Erik Anderson
Point cloud lingo
Last-returns can be 2nd, 3rd, or 4th return.
Last-returns not necessarily reflected from ground but do have higher probaility
*Pulses with only 1-return -> 1st return = Last-return

## Slide 19
From Stoker et al., 2006
Example of Point Clouds for Different Trees

## Slide 20: Waveform Return Detection
Examples of two lidar waveforms (top, green) and returns detected using two different algorithms algorithm (bottom, red). Parrish and Nowak, 2009
Allows flexible signal processing implementations on software side

## Slide 21
Discrete vs full waveform point clouds for two different objects shaded by intensity. Parrish and Nowak, 2009
Discrete Return
Waveform

## Slide 22: Small footprint vs large footprint
Small footprint systems
  Small beam divergence
  Designed for high-res
  E.g. spot size of 15-30 cm at 600 m height
    *Type used for terrain
Large footprint systems
  Large beam divergence
  Canopy mapping
  Typical spot size > 10 m
Image from UNAVCO

## Slide 23: Footprint size on surface impacts positional accuracy. Depends on Flying Height (h) and Beam Divergence ϒ
Image from International Summer School “Digital Recording and 3D Modeling”, Claus Brenner 2006.

## Slide 24: Data Generation

## Slide 25: How do we get a point cloud?
LiDAR raw measurements
  Range measured for each return
  Scan angle for each pulse(angle encoder)
  Aircraft orientation (Inertial Measurement Unit)
  Aircraft position (GPS)
  Time tag (GPS)
Geolocation: combine measurements to derive points in an Earth Centered Earth Fixed frame
  GPS at its frequency (1 or 10 Hz typical)
  IMU at its frequency (e.g. 200 Hz)
  Laser at its pulse rate (e.g. 167 kHz)
  Scanner mirror at its rate (e.g. 30 Hz)

## Slide 26: Example Processing Workflow
Software may differ but overall process will be similar
Post-Processing
QA/QC Procedure

## Slide 27: Calibration: Strip Adjustment
Different survey flight lines (strips)
Roll, pitch, scale offset, etc…
Image adapted from Vosselman

## Slide 28: Example Survey Parameters
Post-Processing
Optech ALTM 33kHz system (older system)
Determining relative positions of GPS, sensor, IMU

## Slide 29: Examples of Lidar-Derived Products
Digital Surface Model (first-returns)
Discrete Return Point cloud

## Slide 30: Ground Point Filtering
For many analyses, desired end-product is a digital elevation model (DEM) of the bare-earth terrain
  Desire only points from ground
  Last-returns are typically used
Filter algorithm
  tries to separate ground / non-ground points
Accuracy of resultant DEM depends heavily on filtering
  e.g. non-filtered vegetation or building points bias elevation

## Slide 31
Image from International Summer School “Digital Recording and 3D Modeling”, Claus Brenner 2006.
What is ground? Filter tries to determine this based on certain criteria. (e.g. local slope)

## Slide 32: Example: TIN Densification Filter
Start with mixed, ground and canopy and build TIN
Example from USGS Ralph Haugerud
Flag points that define spikes (strong convexities)

## Slide 33
Rebuild TIN, flag points on spikes and repeat until done

## Slide 34: Filter Performance
Numerous LiDAR filters have been developed
No single filter is ideal
Performance will vary with terrain
Most do well on smooth terrain
Most have issues on rough terrain & complex urban areas
Still very much an active area of ongoing research.
ISPRS Report on LiDAR filter performance:
http://www.geo.tudelft.nl/frs/isprs/filtertest

## Slide 35: Difficult Ground Features for Lidar Filtering
  Shrubs, especially those below one meter (low-vegetation noise)
  Short walls along walkways
  Bridges
  Buildings with different size and shape
  Hill cut-off edges
  Complex mixed covering
  Areas combined with low and high-relief (jagged terrain)
  [from Meng et. al 2010]

## Slide 36
Filter to get bare-earth DEM

## Slide 37: A bit more on lidar intensity
Changes in path length (R) due to elevation changes result in brighter and dimmer returns (intensities).

## Slide 38: What use is intensity?
Can provide additional information about the surface
  Good for segmentation and classification algorithms
  E.g. buildings and vegetation segmentation

## Slide 39: Intensity-based segmentation of Buildings and Trees

## Slide 40: Segmentation Example (cont’d)
Notice points on walls and roofs underneath canopy correctly classified. Intensity and spin-image geometry allowed us to discriminate objects in overlapping spaces.

## Slide 41: Data Artifacts & Error Sources

## Slide 42: Data Density
Point spacing depends on several factors
  Pulse rate
  Scan angle
  Flying height & speed
  Beam divergence
  Surface properties
Useful relations for mirror scan
Images from Open Topography Portal and UNAVCO

## Slide 43: Data Dropouts
Maximum range decreases dramatically for combination of steep, smooth, wet and black surface properties (rain or fog will attenuate laser pulse to ground)
*Water will still produce a measurable return at near-orthogonal incidence angle
Dark surfaces can absorb pulse (e.g. dark asphalt)
Image from Claus Brenner 2006.

## Slide 44: Multipathing
E.g. Laser pulse reflects specularly from building away from sensor to ground and then back to sensor.
Results in a lower elevation than should be measured causing an outlier.
Sensor places point here causing spurious data.
Image courtesy of Dr, Bharat Lohani, 2010

## Slide 45: Example of Corduroy Artifacts
Inner swath is consistently lower than outer swath where they overlap
Color is elevation
Corduroy effect caused by mirror shift in direction at scan edge
swath misalignment

## Slide 46
Example of corduroy effect in NASA EAARL 2009 first surface Outer Banks data

## Slide 47: Swath Offset in DEM

## Slide 48: Range Walk (issue with discrete return systems)
Aerial photograph showing bright
paint stripes on runway
Notice elevated stripes on runway

## Slide 49: LiDAR Error Budget
1. Laser ranging accuracy 1 –5 cm
2. GPS aircraft positioning error 5 –100 cm
3. Attitude IMU system error 3 –15 cm
4. Terrain type (vegetation “noise”) 1 –100 cm
5. Datum / coordinate shifts 1 –10 cm
Total Error 11 –230 cm (quoted from USGS)
“Research grade lidar” : 15-30 cm horizontal; < 10 cm vertical over flat terrain and standard flying height

## Slide 50
Vertical error caused by Lidar horizontal error on steeply sloping terrain.
Vertical error increase with slope of the terrain ; Hodgson et. al, 2003

## Slide 51: Comparisons of LiDAR to other measurement techniques *
 | GPS | InSAR | LiDAR | TLS
Sample Density | 1 site/10 km2 | 10,000 pixels/ km2 | 1-10 hits/ m2 | 1000 hits/ m2
Position Precision | 1-20 mm | 2-3 m | 5-15 cm | 0.6-5 cm
Change Detection | 1 mm | 1-2 cm | 10 cm | 1 cm
Scale | Global | 100 km | 10-100 Km | 1 km
* Ball park numbers for typical applications from UNAVCO

## Slide 52: System Examples

## Slide 53: Optech ALTM Gemini - near-IR (1064 nm) laser - up to 167 kHz pulse repetition frequency - Discrete return: up to 4 per pulse Max flying height of ~4500 m above ground at lowest pulse repetition frequency
Gemini system mounted in aircraft

## Slide 54
Dense Gemini data collected over UC Berkley stadium by NCALM. At 167 kHz Can get > 10 pts/m2
Northern California (from GeoEarthScope)

## Slide 55: SHOALS-3000 Bathymetric Lidar
Developed by Optech Inc. USACE coastal charting group uses this system
SHOALS laser generates Near-IR and Blue Green
Infrared pulse reflects from water surface
Blue-green penetrates water & reflects off bottom
Return blue-waveform compared to IR to determine water depth
Specs:
Max Depth 60 m
*depends on water clarity
- 20 kHz topo-laser
- 3 kHz bathy-laser
- 200 to 400 m nominal fly height

## Slide 56
SHOALS bathymetry data collected by UASCE along Panama City Beach FL
Borrow Pits
Data drop-outs in shallow surf zone

## Slide 57: NASA/USGS EAARL
EAARL Nominal Specs. (from USGS 2010)
Short laser pulse
Narrowed receiver field-of-view (FOV)
Full waveform digitizer
Real-time signal processing software to extract returns
Short pulse helps detect terrain under short vegetation and shallow water.
532 nm Bathymetric LiDAR system, 10 kHz pulse rate

## Slide 58
Mosaic of 2001-2002 & 2006 Florida Keys
EAARL Submerged Topography (from NASA)

## Slide 59
EAARL 2009 first surface data of Ocracoke Island on Outer Banks

## Slide 60: Coastal Area Tactical-mapping System (CATS)
Photon-counting system
  Operates at blue-green light (532 nm)
    water penetration
  Multi-channel
  Uses two rotating prisms instead of mirror to scan
  Designed for target detection in shallow surf zone (< 5 m)
  UF system developed for Office of Naval Research

## Slide 61: CATS Multi-Channel

## Slide 62: CATS water penetration test
Kris Shrestha

## Slide 63: Thank you!
Any Questions?

## Slide 64: Gaussian Shaped Laser Pulse
Typical Characteristics
trise = pulse rise time
tp = pulse width; 10 ns ( 3 m @ speed of light)
Ppeak = 2000 Watts
*Separation of two returns depends on pulse width and receiver response
Signal Amplitude
Time t
T0 pulse
Ideal return pulse
Tl
Leading edge of pulse