## Slide 1: Managing change at a dune landscape
Ondrej Mitas, NHTV, Netherlands
Helena Mitasova, Katherine Weaver, Gene Brothers
North Carolina State University

## Slide 2: North Carolina Outer Banks
1903 Wright brothers
Cape Hatteras
0 10km
Atlantic Ocean
Nags Head
Pea Island
Barrier islands
Favorite tourist
destination
Dynamic landscape:
sand redistributed
by wind, waves, storm surge
Vulnerable:
coastal erosion,
sea level rise, breach
Notes: The Outer Banks are historically known for their constant battering from intense storms and sea level rise which expose vulnerable areas such as the Isabel Breach south of Cape Hatteras created during Hurricane Isabel. These storms also destroy personal properties such as this picture of a porsche being submerged under sand and overwash. And with the steady increase of sea level, infrastructure that was once a safe distance away are merely feet away from the shoreline (for example the moving of the Cape Hatteras Lighthouse in 1999). This area is also well known for its high dunes that once permitted the Wright Brother’s to successfully take flight in 1903.

## Slide 3: Jockey’s Ridge: The largest active sand dune on the east coast

## Slide 4
Visitors,
participants in the survey,
come from close metropolitan areas
The most visited state park in NC
1.5 million visitors per year
Washington DC
New York City
Philadelphia
Raleigh
Richmond, Norfolk

## Slide 5: Jockey’s Ridge history
1932: all sand
1940: sand, new vegetation
2003: post Isabel lot of vegetation
1879
1932
1862
State park established in 1974 to save the dune from development

## Slide 6
2003
Minigolf castle buried by the dune in 80s emerged in 2000
2000 2002
Sand transport: management problems

## Slide 7
Efforts to stop the dune
Stabilization fences were
installed but the result was mixed:
Dune was losing its unique shape

## Slide 8: Surveying Jockey’s Ridge
Airborne
LiDAR
LiDAR data by NOAA, USACE; RTK GPS mapping and modeling by Geodynamics llt., NC

## Slide 9: Dune migrating out of the park
Jockey’s Ridge:
active dune system within
fixed state park boundaries
How long will it stay within the park boundaries?
What is the rate of migration?
Migration measured as change in location of dune crests extracted from time series of Digital Elevation Models (DEMs)
200m
Dune migration
1974-2008

## Slide 10
1974
1995
2001
2008
0 200m
Rate of migration and transformation
Notes: 10
10

## Slide 11
As the dune migrates it loses sand on
windward side and gains it at leeward side.
The sand stays within the park except for
areas where the dune reached its borders.
N
1974: peak at 42 m
2001: peak at 23 m
sand
gained
stable
sand lost
a
b
c
d
e
a
b
c
d
e
Sand transport

## Slide 12
South dune encroachment on a house and street.
Managing dune migration and height
Removal of the south dune and disposal at windward side in 2003

## Slide 13
2008: 21 m
1974: 33 m
1949: 42 m
2008: 21 m 1950: 42 m
N
sand
gained
stable
sand lost
Change in dune height
Since 2004 dune height has stabilized at 21 – 22 me
Notes: 13

## Slide 14
2008: 21 m
1974: 33 m
1949: 42 m
2008: 21 m 1950: 42 m 1917 20 m ?
1930: 32 m ?
1917: 20 m ?
N
sand
gained
stable
sand lost
Change in dune height
High active dune: result of bad land management?
Landscape going back to its more stable form
Notes: 14

## Slide 15
1945
2009
1974
Chart: Year
| 1932.0 | 1945.0 | 1955.0 | 1962.0 | 1974.0 | 1988.0 | 1998.0 | 2007.0 | 2009.0
Development | 1.2373 | 2.5383 | 4.6136 | 6.6044 | 15.107 | 24.1823 | 25.8923 | 32.2665 | 33.4832
Sand | 237.5546 | 219.7477 | 212.2196 | 186.5939 | 189.3041 | 164.804 | 140.131 | 148.5218 | 136.2018
Vegetation | 56.436 | 72.6299 | 78.2197 | 101.995 | 90.7825 | 106.2094 | 129.172 | 114.4096 | 125.5091
Dramatic change in land cover
46% sand 42% vegetated 11% developed
74% sand 25% vegetated 1% developed
64% sand 31% vegetated 5% developed

## Slide 16
Post cards show very little vegetation in 1912 - 1977
Dune past captured on postcards

## Slide 17
1905 Wright brothers’ photos:
dunes were destroying the vegetation Vegetation lost to dune between 1998-2007
Vegetation gradually starts taking over, in 2010 vegetation grows over slip face,
Dune – vegetation interaction
Vegetation is now limiting the dune migration, sand disposal stabilized the dune height
2003 2005 2010

## Slide 18
March 2010 after a storm
jumping and rolling down the slip face
Visitor impacts
Data do not support the notion of negative visitors impact on dune height:
dune was losing elevation even before the park was established
height has stabilized over past 5 years when the number of visitors reached the highest levels
extreme storm in 1962 and gradual increase in vegetation limiting the sand supply probably triggered the dune decline.

## Slide 19
august 2005 during data collection
Visitor preferences
Visitor’s survey: 200 visitors in July, August, October of 2005
What do visitors value about the dune in terms of features and processes?
Change was perceived as valuable/positive if natural

## Slide 20
August 2005
Conclusions
Vegetation is now limiting the dune migration
Sand disposal stabilized the dune height
Stabilization measures limited to boundary areas preserved the dune morphology
Positive visitor experience is contingent upon the perception that the changes are natural
Management focus is on preserving processes rather than features: living landscape

## Slide 21
march 2010 - spring break, it can be crowded and deserted at the same time
Thank You