## Slide 1: Coupling Open Source GIS with tangible interface and immersive visualization for collaborative geodesign Helena Mitasova, Anna Petrasova, Vaclav Petras, Brendan Harmon Center for Geospatial Analytics, North Carolina State University

## Slide 2: Collaborative Geodesign
Motivation for tangible interface and large scale visualization:
allow participants with different backgrounds to generate ideas
present baseline information in intuitive and engaging way
change landscape easily
get instant feedback on impacts of changes

## Slide 3: Tangible Landscape
Hardware: projector, Kinect, computer, 3D physical model
Software: Kinect for Windows SDK, GRASS GIS, custom python script

## Slide 4: Tangible Landscape set up
Laboratory and mobile systems

## Slide 5: Creating 3D models
Kinetic sand model from contours and a 3D printed model

## Slide 6: Creating 3D models
CNC routing for models and molds

## Slide 7: Creating 3D models
Solid models with molded kinetic sand layer

## Slide 8: Coupling with GRASS GIS
Open source GRASS GIS:
general purpose GIS and geospatial science computing platform
Custom Python scripts:
coupling with scanner, data display, analysis, and modeling

## Slide 9: Data: Centennial Campus
Rapidly urbanizing area: fields transformed into research campus
3D data acquired by lidar in 2001 and 2013

## Slide 10: Landscape modification
Modifying the landscape with feedback on elevation change
100m

## Slide 11: Surface water flow
Exploring the impact of development on runoff

## Slide 12: Dam Break
Dam broke on the Lake Raleigh in 1996 during Hurricane Fran
Dam break flooding impact: current and with road removed

## Slide 13: Dam Break
Dam break simulation under the current topographic conditions

## Slide 14: Trails
Least cost path over cumulative cost surface
Blocks define waypoints
Sand layer modified to explore grading, bridges

## Slide 15: Viewsheds
Planning waypoints with views: block defines viewing site

## Slide 16: Fire spread
Fire spread modeling using fuel estimates from lidar data:
Exploring effectiveness of a firebreak

## Slide 17: Solar radiation
Solar radiation modeling: summer solstice dynamics
Virtual 3D dynamic model and projected over 3D physical model

## Slide 18: Bringing the digital models to large screen
Large scale, interactive 3D visualization with GRASS GIS

## Slide 19: GIS for landscape architects projects
The best explored ideas are then optimized using
GIS modeling and design

## Slide 20: Conclusion
Tangible Landscape systems can provide 3D sketching with real-time feedback for geodesign
Book: Tangible modeling with open source GIS Springer, coming later in 2015
http://geospatial.ncsu.edu/osgeorel/
Photos and videos on Google+

## Slide 21: Interactive viewsheds
Exploring views from different viewing sites

## Slide 22: Interactive trails
adding a waypoint